Describe open-ended prefetcher

For the open-ended prefetcher, we used a global history buffer (GHB) inspired approach. Our structure for the prefetcher consists of a global history FIFO queue, implented as a linked list, and a separate two-element queue containing the most recently observed cache accesses. This prefetcher works on deltas between subsequent memory access addresses in order to account for sequential and incrementing access patterns. On every call to the prefetch algorithm, both the two-element queue and the global FIFO queue are updated with a delta calculated from the current access address. The global FIFO queue is then searched in reverse order for the first pattern that matches the two-element queue. If discovered, the linked list element before the matched two-element queue is taken as the delta to add to the current access address to yield the prefetch address. Essentially, this algorithm works on the principle of pattern matching, partially similar in idea to the GaP branch prediction pattern matcher. This prefetching algorithm is capable of accurately predicting memory access patterns that have alternating deltas, a case that would cause stride to fail due to the irregular location accesses. This algorithm is also scalable because both the global history FIFO queue could be increased or the two-element queue could be made deeper. We have chosen these sizes to work well with the cache specified in cache-lru-openend.cfg. A CACTI simulation was used to analyze the physical overhead introduced by this prefetcher.

Cache:
Data
Height(mm) : 0.258213
Width(mm) : 0.186667
Area(mm2) : 0.0481999
Total dynamic read energy (nJ) : 0.0181207
Time (ns) : 0.28507
Tag
Height(mm): 0.0369555
Width(mm) : 0.0211796
Area(mm2) : 0.000782704
Total dynamic read energy (nJ) : 0.000409321
Tag (ns) : 0.155352

Prefetcher
Access time(ns) : 0.118515
Total dynamic read energy (nJ) : 0.000312963
Total leakage power of bank (mW) : 0.0286315
Height by width (mm) : 0.0196443 x 0.0130175

Evident in the above results, the prefetcher adds slight overhead. The amount of extra power lost and additional area required is on the order of another tag structure using the specified cache. However, the prefetcher does introduce extra delay also on the order of a tag access, which is comparable to the data access time of the cache. If the prefetcher is activated on every cache access, the total access time would be increased about (0.118515 / (0.28507 + 0.155352)) = 27%. Given that the prefetcher decreases the average miss rate between the three microbenchmarks to below 2.1% from a baseline average miss rate of about 2.3%, it may be more beneficial to include the prefetcher if time penalties are substantial for a miss rate. Hence, the decision to include the prefetcher depends heavily on the data transmission time between the L2 cache, the access time of the L2 cache, and the time penalty resulting from L1 and L2 misses.